## Slide 1
SIH 2026
SIH26161
Dam Break Inundation Modelling
Should we pick it? An evidence-based read of what the Government of India has already built — and what it hasn't.
Sponsor National Technical Research Organisation (NTRO)
Theme Disaster Management · Software · Idea deadline 20 Sep 2026
Research date 29 Aug 2026
Notes: Verdict up front: worth picking, conditionally. The PS is not what we assumed and the duplication risk is worse than feared, but a real gap survives.

## Slide 2
THE SHORT VERSION
Four numbers that decide this
6,628
specified dams already registered, inspected and inundation-mapped under the Dam Safety Act
verified
10 Mar 2026
RBSD went live — the government's own dam-break and population-at-risk dashboard
verified
12 days
Sentinel-1 nominal revisit outside Europe. A breach develops in minutes.
verified
5 weeks
for the NDMA team to reach the 2015 Phutkal landslide dam. That is the gap.
verified
Verdict: pick it — conditionally.
Highest ceiling of the four PSs under consideration, and the highest floor risk. The two conditions are on the last slide.
Sources: PIB Backgrounder 15 May 2026 · GIS Resources / OpenGov Asia · Copernicus SentiWiki · SANDRP 2015

## Slide 3
PART 1
The PS is not what we assumed
On the record
SPONSOR
NTRO — not CWC / Jal Shakti
THEME
Disaster Management · Software
DEADLINE
20 September 2026
IDEA CAP
500 submissions
DATA NAMED
Sentinel / Landsat + ASTER / SRTM DEM
What it literally demands
Smoothed Particle Hydrodynamics and 'Delf3D', and a comparison of the two scenarios
Dam break AND river blockage analysis — the background is dominated by natural dams: Rishi Ganga 2021, Phutkal 2015, Kosi 2008
Loss and damage analysis from the sudden water surge
A dashboard GUI handling large data volumes; output as .shp or .kml
A near-real-time flood analysis framework via Google Earth Engine
Demonstration on a real Indian river and dam, open-source data
verified
Verbatim from the official PS text (sih.gov.in/sih2026PS), corroborated across two independent mirrors.
Notes: Biggest single surprise. Everyone will assume this is a CWC flood-forecasting problem. It is an intelligence-agency HADR tooling problem, and it names two heavyweight solvers.

## Slide 4
PART 1
Scope discipline: what is in, what is not
EXPLICITLY REQUIRED
Automatic dam-break + river-blockage simulation
SPH and Delft3D, compared
Loss and damage analysis
Dashboard GUI, large data volumes
.shp / .kml export
GEE near-real-time framework
Real Indian river + dam demo
NEVER MENTIONED
Evacuation routing
Shelter allocation
Alert dissemination / SMS
Real-time gauge or telemetry ingestion
Live operational deployment
Any accuracy target
Any specified river or dam
Consequence: everything we wanted to add — roads, evacuation priority, shelters — is value-add, not a substitute. A build that ships a gorgeous evacuation dashboard and no SPH / Delft3D comparison reads as non-compliant to an NTRO panel.

## Slide 5
PART 2
What the government already operates
C-FLOOD
CWC + C-DAC + NRSC
48 h village-level inundation forecasts, 3 basins, ANUGA on NSM HPC. Live 2 Jul 2025.
RBSD
C-DAC FOR NDSA
Dam-break analysis, inundation depth and timing, Population at Risk and Infrastructure at Risk.
DHARMA + NETRA
NDSA
All 6,628 dams registered; about 13,000 inspections a year; AI review built with the Navy's WESEE.
CWC FF network
CENTRAL WATER COMMISSION
360 forecasting stations, 7,000+ forecasts a year, FloodWatch app out to 7 days.
SACHET
NDMA + C-DOT
CAP alerting in all 36 States/UTs. 134 billion SMS. Cell broadcast rolling out.
Glacial lake watch
CWC / NRSC / NDMA
2,843 lakes monitored monthly on Sentinel via GEE. NGRMP covers 189 high-risk lakes.
All six verified from PIB releases, official portals and the operating agencies' own pages.

## Slide 6
PART 2
C-FLOOD is not our competitor
Checked live on 29 Aug 2026
Public map at inf.cwc.gov.in, no login needed to browse
Depth classes only: under 0.5 m / 0.5 to 1.5 m / over 1.5 m
Three-day tabs, refreshed every 3 hours, English / Hindi / Odia
Mahanadi, Godavari, Tapi — 3 of 20 basins
Runs ANUGA, an open-source 2D shallow-water solver, on National Supercomputing Mission hardware
Claims 15 to 20 cm depth error in floodplains
The banner on the portal
“Inundation is based on rainfall, river discharge and tide.”
So it has no breach mode
A dam-break scenario engine does not duplicate C-FLOOD. But “another 2D inundation viewer with a village layer” absolutely does — and theirs runs on a supercomputer.
Free win: if we build on ANUGA we are using the government's own solver. That is the answer to “why should we trust your model?”

## Slide 7
PART 2 · THE UNCOMFORTABLE ONE
Our original pitch is already built
RBSD
Rāshtriya Bāndh Surakshā Darpan
Built by C-DAC for the National Dam Safety Authority. Launched 10 March 2026 alongside NETRA.
What it already does
Presents Dam Break Analysis results as maps and dashboards
Inundation extent, depth AND timing
Population at Risk (PAR)
Infrastructure at Risk — settlements, roads, bridges, critical facilities
Explicitly to support evacuation planning and Emergency Action Plans
That is our “flood sim, population exposure, decision-support dashboard” idea — shipped by C-DAC, for the national regulator.
rbsd.ndsa.gov.in is a login wall — checked 29 Aug 2026. Gated, precomputed, and scoped to specified dams. That is where the daylight is.
Notes: Say this ourselves in the SIH pitch. Owning the comparison beats being ambushed by a judge who knows RBSD exists.

## Slide 8
PART 3
Solved, half-solved, open
ALREADY SOLVED — DO NOT REBUILD
Riverine inundation forecasting (C-FLOOD)
Dam-break PAR dashboards (RBSD)
Dam registry and inspections (DHARMA)
Last-mile alerting (SACHET)
Post-event extent mapping (NRSC, Copernicus)
PARTLY SOLVED — HEADROOM
Dam-break output is static and login-gated
Single deterministic breach estimate, no ensemble
C-FLOOD covers 3 of 20 basins, no breach mode
Glacial-lake watch is monthly and area-based only
GENUINELY OPEN
Impoundments outside the regulatory perimeter
Detection to decision in hours, not weeks
Breach ensembles, confidence-banded arrival times
Time-varying road isolation analysis
No national open shelter-capacity dataset
The Dam Safety Act governs specified dams over 15 m. A landslide dam that formed last week is not one.

## Slide 9
PART 3 · THE OPENING
The hazard class nobody owns
5+
weeks
before the NDMA team reached the Phutkal landslide dam in Zanskar, 2015. Roughly 50 days elapsed before channel-cutting work began.
Why nothing covers it
No DHARMA record — it is not a specified dam
No Emergency Action Plan
No precomputed inundation map, so no RBSD entry
No gauge, no rating curve, no telemetry
No surveyed geometry and no breach parameters
And the PS names these events itself: Rishi Ganga 2021, Phutkal 2015, Kosi 2008
“NDSA has a plan for all 6,628 specified dams. Nobody has a plan for the dam that formed last Tuesday.”

## Slide 10
PART 6
“Real-time satellite river level” does not exist
Chart: Satellite revisit vs a breach that develops in minutes
| Sentinel-1 SAR (India) | SWOT altimetry | Sentinel-3 altimetry
Revisit (days) | 12 | 21 | 27
Accuracy is no better
Sentinel-3 river level RMSE 1.29 m
Jason-3 river level RMSE 3.13 m
SWOT 0.29 m — best, still 21-day repeat
Use the right tier
Satellites do discovery, over days. Gauges, reservoir telemetry and rainfall do triggering, over minutes. A precomputed scenario library does the answering, in seconds.
Differentiator: most competing teams will claim real-time satellite monitoring. It is false, and an NTRO panel knows the revisit numbers. Being the team that refuses the claim is worth more than the claim.

## Slide 11
PART 5
The SPH requirement, solved honestly
The problem
1.5 s
of physical time is what 1 million SPH particles buys — about 15 minutes on a GPU. A 6-hour flood over 50 km is off by orders of magnitude.
The resolution
SWE-SPH — 2D depth-averaged smoothed particle hydrodynamics
A published family built for exactly this: dam breaks, tsunamis, levee breaches. It computes only in wet cells, so it adapts to an unknown inundation extent. Implement it in PySPH — which supports the shallow water equations, is BSD-licensed, and is developed at IIT Bombay Aerospace.
ANUGA
PRIMARY ENGINE
Python-native, pip-installable, and the same solver C-DAC runs inside C-FLOOD. Carries all scenarios and exposure analytics.
PySPH SWE-SPH
LAGRANGIAN COMPARISON
Near-field domain only — the breach plus the first few kilometres. Satisfies the named SPH requirement without faking it.
Delft3D-FLOW
THIRD COMPARISON
Kernels are GPLv3 with a free GUI. Prebuild one benchmark case before the finale; present it as precomputed.
All three checked against the Ritter analytical dam-break solution — roughly an hour of work, and the difference between “we made a simulation” and “we validated one”.

## Slide 12
PART 4
Every input is open — except two
LAYER
SOURCE WE WOULD USE
ACCESS
Terrain
FABDEM 30 m bare-earth, Copernicus GLO-30, CartoDEM
Open / free registration
Population
GHS-POP 100 m, best performer for Indian villages; Census 2011 PCA
Open
Buildings
VIDA combined Google + Microsoft + OSM, 2.7 bn footprints
Open
Roads & POIs
OpenStreetMap via OSMnx / Geofabrik
Open, ODbL
Villages
Census 2011 polygons — Datameet, SHRUG, AIKosh
Open
Dams
National Register of Specified Dams 2026 (NDSA PDF)
Open
Reservoir levels
India-WRIS, data.gov.in daily CWC series, Kerala live JSON
Open
Imagery
Sentinel-1 / 2, Landsat, Bhuvan NOEDA
Open / free registration
The two exceptions: reservoir bathymetry and breach parameters are not published for Indian dams. Both have accepted estimation routes — stage-storage from the DEM, and Froehlich (2008), which CWC recommends. Say so out loud; it converts a weakness into method.

## Slide 13
PART 7
The pipeline
1
Hazard ingest
GEE Sentinel-1/2 change detection, the dam register, or an analyst-drawn polygon
2
Geometry & volume
DEM fill-to-outlet gives the stage-storage curve and impounded volume
3
Breach ensemble
Froehlich 2008 plus two alternatives, giving pessimistic / central / optimistic hydrographs
4
Dual-solver engine
ANUGA full domain, PySPH SWE-SPH near field, both checked against Ritter
5
Depth & arrival time
Rasters per timestep. Arrival time is the output that actually drives decisions
6
Exposure
GHS-POP, village polygons, building footprints, giving PAR and loss/damage
7
Road isolation
OSMnx graph, edges cut by depth per timestep: when each village loses its last exit
8
Priority list
Ranked by isolation time, population and egress, with ensemble confidence bands
9
Outputs
.shp / .kml, an EAP-template-shaped PDF, and a CAP-conformant payload
Step 7 is the differentiator — no operational Indian system computes which village loses its last road out, and at what minute.

## Slide 14
PART 7
What must work, and what can wait
CORE MVP — NON-NEGOTIABLE
DEM, impoundment volume, Froehlich hydrograph
ANUGA run producing depth and arrival-time rasters
Per-village population and buildings exposed
.shp / .kml export — a literal PS deliverable
Time-slider map
Ritter validation plot
Two prepared cases: one engineered dam, one natural blockage
ONLY IF TIME PERMITS — IN THIS ORDER
Road isolation analysis — highest marginal judge value
PySPH SWE-SPH comparison
GEE change-detection notebook (PS deliverable iv)
EAP-shaped PDF generator
CAP payload for SACHET ingestion
3D flythrough render
Uncertainty bands surfaced in the UI
Cut without hesitation: shelter optimisation (the data does not exist), user accounts, a mobile app, and anything that actually sends alerts.

## Slide 15
PART 10
The five risks that actually bite
Non-compliance with SPH + Delft3D
Critical
Build SWE-SPH in PySPH as a real second solver and prebuild one Delft3D case. Do this before touching the UI.
Reading as an RBSD clone
Critical
Lead with ad-hoc impoundments and isolation time. Name RBSD in our own deck and state what we add.
No breach parameters exist
High
Make it the feature: a three-equation ensemble reported as a confidence band, never a single number.
30 m DEM ceiling on accuracy
High
FABDEM bare-earth, channel burn from OSM waterways, and a Manning's n sensitivity run shown on screen.
Simulation too slow to demo live
High
Precompute the scenario library. That is the correct architecture anyway; emergencies cannot wait for a solver.
Full ten-risk register, each with a hackathon mitigation, is in Part 10 of the written report.

## Slide 16
PART 12
Why the obvious pitch scores worst
Chart: 
| Pure hydrodynamics | Hydro + visualisation | Hydro + generic decision support | Hydro + ad-hoc impoundments + isolation
Score out of 80 | 43 | 44 | 39 | 66
The inversion
Our instinct — that the opportunity is the downstream decision-support layer — scores worst in its generic form, because RBSD already is that layer.
The same instinct scores best once it is aimed at hazards nobody owns, and at the one analytic — time-varying road isolation — that no operational Indian system provides.
Scored across novelty, technical depth, feasibility, judge appeal, government relevance, differentiation, data availability and PS compliance.

## Slide 17
PART 13
Against the other three on our shortlist
SIH26161
Dam Break · NTRO
Highest ceiling, highest variance. Needs real hydraulics skill and weeks of prep before the finale.
our pick
SIH26012
Cadastral extraction · MoRD
Lives or dies on securing labelled drone imagery. Crowded with CV teams. Verify data access this week.
SIH26013
Geospatial harmonisation · MoRD
Low variance, low ceiling. Data-light and safe, but schema reconciliation does not demo well.
SIH26021
Honey Chain · MSME
Lowest technical depth, highest crowding. Choose only to optimise for a safe finish.
Before committing: verify the PS text on the official portal, try to register for RBSD, and pip-install ANUGA and PySPH today. If either install fails on our machines, the whole plan changes.

## Slide 18
THE CALL
Pick it, on two conditions
01
Someone owns the hydraulics
At least one team member must be genuinely comfortable with shallow-water equations, CFL stability, boundary conditions and Manning's n. Without that, the SPH requirement is a wall we hit at hour 20.
02
We accept the reframing
If the plan is “flood map plus population dashboard”, decline this PS. We will be measured against RBSD and lose.
What we build
A rapid consequence-assessment engine for impoundments nobody has modelled — landslide dams, moraine-dammed lakes, blocked reaches — with arrival time and road isolation as the headline outputs, not flood extent.
“34-minute evacuation window for 1,240 people” beats any heat map.
Full evidence, citations and the seven pre-commitment checks are in the written report.
Notes: Two conditions, both hard. If either fails, SIH26013 is the low-variance hedge.